## Slide 1: Development of a Symbolic Regression-Based Model for Leading Edge of Film Cooled Gas Turbine Blade

## Slide 2
3D CAD Geometry
Meshing Methodology
CFD Validation
Parametric Geometry Design
Parameter Selection and Parameter
Ranges
Model Training
(Symbolic Regression)
Results
Model Testing & Comparison with CFD Results
Project Workflow

## Slide 3: 3D CAD Geometry
The geometry was designed to enable periodic analysis, since the paper does not specify the number of holes.
The validation is based on the study “Overall Effectiveness for a Film-Cooled Turbine Blade Leading Edge With Varying Hole Pitch. ”
K = 1.04  0.06 W/m.K (Polycast 287)

## Slide 4
Meshing
View from top

## Slide 5
Solid
Solid
Solid
Fluid Domain
Fluid Domain
Fluid Domain

## Slide 6: Boundary Conditions
Mainstream velocity was maintained at a nominal value of 15 m/s.
Tu levels measured at 5%, with a turbulence length scale of 2.3 cm at the location of the model
Typical 𝑇∞ values were near 300 K. The coolant was simulated using N2​ gas at 200 K in order to maintain a constant DR of 1.5 for all test conditions.
The cold gas then passed through a plenum which served to evenly distribute the gas along the span of the model.
turbulence effects were modeled with the Realizable k–ε and Menter SST k–ω approaches
(Blowing ratio ) M = 2

## Slide 7
Results
Experiment
CFD

## Slide 11
Parametric Study
Coolant Inlet
Translational Periodicity
Outlet
Mainstream Inlet

## Slide 12
Meshing For Parametric Geometry
View From Front
View From inside of the Geometry

## Slide 13
Impingement Hole
Side Hole Angle
Pitch
Cooling Hole Diameter
Design variable | Symbol | Unit | Lower bound | Upper bound
Cooling Hole Diameter | D | mm | 2 | 6
Pitch | P | mm | 22 | 50
Impingement Hole Diameter | ID | mm | 3 | 12
Side Hole Angle | ∅ | ° | 15 | 70

## Slide 14
Training Samples
The dataset consisting of these samples was utilized to train the symbolic regression-based mathematical model.
These are only the first 31 samples. In total, there are 79 samples.
The model was built in Python using the PySR library.
=

## Slide 15
Testing Samples
Testing samples were used to compare the CFD results with the model predictions obtained from the training samples.

## Slide 18
The graph did not turn out as expected. I aimed for a result similar to the example below, but it did not work as intended. Although I would like to continue working on this project, I currently do not have enough time. I plan to complete it after my internship.
Example